APES Math Review Answers

1. a. 2,000 kcal; b. 8.37 x 106 J = 8.37 MJ; c. 7,940 Btu; d. 11.9 minutes. 

2. b. The second law of thermodynamics prevents 100 percent conversion of heat to mechanical or electrical energy. A typical coal-fired power plant operates at about 33 percent efficiency, meaning that only one-third of the energy in the coal is converted to electricity. 

3. a. 1,941 ccf; b. $1,748; c. 9.2 years 

4. a. 9.57 MBtu; b. 8 percent; c. 1,200 

5. a. 2,190 kWh; b. 21.9 percent; c. 45.7 m2 

6. 498 tons 

7. a. 4,000; b. Answers vary 

8. Battery energy: 4.5 Wh = 4.5 x 103 kWh.
Cost per kWh: $1.00 / 4.5 x 103 kWh = $222/kWh.
Comparison: Electrical energy from the battery costs $222 / $0.10 = 2,220 times as much as that delivered by the power company. 

9.

| Fuel | Price1 | Energy Content of Fuel | Cost per MBtu | Cost of Home Heating1 |
| --- | --- | --- | --- | --- |
| Nat. gas | $1.14/ccf | 1,030 Btu/cf | $11.07 | $1,660 |
| Propane | $1.69/gal | 92 kBtu/gal | $18.37 | $2,755 |
| Fuel oil | $1.93/gal | 133 k Btu/gal | $14.51 | $2,177 |
| Electricity | $0.10/kWh | 3,412 Btu/kWh | $29.31 | $3,5173 |

Notes
1. Prices quoted are for home delivery of respective fuels at rates available in the north central U.S. in 2005. 
2. Computations assume a heating requirement of 120 MBtu for the "average" home in the northern U.S. Efficiencies of 80 percent are assumed for gas or oil furnaces. Heat from electricity is assumed to be delivered at 100 percent efficiency in the home. 
3. Homes designed for electric heating are usually insulated more thoroughly than those designed for gas or oil.